## Slide 1: HIDDEN AND EXPOSED TERMINAL PROBLEM
Wireless Networks

## Slide 2: Virtual carrier sensing
First exchange control frames before transmitting data
  Sender issues “Request to Send” (RTS), incl. length of data
  Receiver responds with “Clear to Send” (CTS)
If sender sees CTS, transmits data (of specified length)
If other node sees CTS, will idle for specified period
If other node sees RTS but not CTS, free to send
Notes: Like we said in class, CTS is like token, except that every host has its own.

## Slide 3: Hidden Terminal Problem
A and C can’t see each other, both send to B
RTS/CTS can help
  Both A and C would send RTS that B would see first
  B only responds with one CTS (say, echoing A’s RTS)
  C detects that CTS doesn’t match and won’t send
C
B
A
Notes: Can’t see each other because neither C is in A’s range, nor A is in C’s range, but B is in both of their ranges

## Slide 4: Exposed Terminal Problem
B sending to A, C wants to send to D
As C receives packets, carrier sense would prevent it from sending to D, even though wouldn’t interfere
RTS/CTS can help
  C hears RTS from B, but not CTS from A
  C knows its transmission will not interfere at B’s receiver
  C is safe to transmit to D
C
B
A
D
Notes: B is sending to A, and C is in B’s range